## Slide 1: Converter Design
Converter Design

## Slide 2: System requirements
Converter input | 
 | 300.4 [W]
 | 45 [V]
 | 8.67 [A]
Converter output | 
 | 90 [V]
 | 24 [V]
 | 12.5 [A]
Converter input | 
 | 300.4 [W]
 | 45 [V]
 | 8.67 [A]
Converter output | 
 | 90 [V]
 | 24 [V]
 | 12.5 [A]
Ripples | 
 | 0.5 [%]
 | 0.1 [%]
 | 10 [%]
PV system specification | 
Minimum string length | 4
Maximum string length | 15
Ripples | 
 | 0.5 [%]
 | 0.1 [%]
 | 10 [%]
PV system specification | 
Minimum string length | 4
Maximum string length | 15
Notes: How did we select the values
Input from PV panel
Output from inverter voltage and # of panels
# of panels from minimum and maximum duties
Ripples so we dont mess with the PV panel

## Slide 3: Selection of topology
Non-inverting buck-boost converter
Notes: Capabilities of both higher and lower output voltage
2 or 4 MOSFETs
Bidirectional opportunities
Lower (conduction) losses

## Slide 4: Passive components Sizing
Calculated using the ripples
Defining worst case conditions
Depends on switching frequency
Notes: Did a voltage sweep to determine worst case

## Slide 5: Passive components Sizing

## Slide 6: Passive components Selection
Minimum 20% margin was included
Reused inductor
Component | Theoretical value | Implemented value | Voltage rating
Input capacitor | 1540µF | 1880µF | 100V
Output capacitor | 130µF | 820µF | 250V
Inductor | 1.3mH | 1.93mH | -
Notes: Input cap is 4*470uF
Calculation mistakes lead to wrongly selected cout

## Slide 7: Power circuitry
Discharging resistors.
Protection diodes.
High frequency capacitors.

## Slide 8: Driver circuitry
Optocouplers for isolation.
Decoupling capacitors.
Current limiting resistors.

## Slide 9: Sensor circuitry
Notes: Optical unity-gain amplifier – voltage sensors
Hall effect – current sensor

## Slide 10: Power supplies
External supplies
Linear 5V voltage regulator
Isolated 12V TRACO supplies
LED at every supply line

## Slide 11: Future work
Hardware improvements
Inductor design
PCB improvements
Converter’s efficiency
V/I controller

## Slide 12: Conclusion
Add something about the general intro?
What went good
What went bad
What did we learn