## Slide 1: Questions
Group 670

## Slide 2: Minimum and maximum number of panels
Minimum panels:
Boost mode.
Duty limitation for control ease.
is set to be 0.6 under STC,
= 4 modules.
Maximum panels:
Buck mode.
Current limitation.
has been set to 12.5 A.
= 15 modules.

## Slide 3: Why are there more losses in diodes than MOSFETs
MOSFET
MOSFET losses are calculated with the internal resistance.
Therefore there is a quadratic relationship between losses and current.
Project FETs : 20mΩ.
Diode
Diode losses are calculated with the forward voltage.
Therefore there is a linear relationship between losses and current.
Common forward voltage: 0.7V
MOSFET losses are then lower up to 36A.
* might vary with temperature

## Slide 4: DCM
MOSFETs do not prevent reverse current like a diode would.
DCM mode is never reached when working with the 4 transistors.
Instead current would be negative through the inductor.

## Slide 5: DCM
MOSFETs do not prevent reverse current like a diode would.
DCM mode is never reached when working with the 4 transistors.
Instead current would be negative through the couil.

## Slide 6: DCM
MOSFETs do not prevent reverse current like a diode would.
DCM mode is never reached when working with the 4 transistors.
Instead current would be negative through the couil.

## Slide 7: DCM
MOSFETs do not prevent reverse current like a diode would.
DCM mode is never reached when working with the 4 transistors.
Instead current would be negative through the couil.

## Slide 8: DCM
DCM mode depends on output voltage and power generated.

## Slide 9: Limiting resistance
Higher
- lower instant current.
- longer turn-on time.
Turn-on time calculated to be 0.1% of cycle.
Possible to have different turn-on, turn-off times.
DRV
PWM
OUT H
OUT L

## Slide 10: Discharging resistor

## Slide 11: MPPT – Running frequency
Low frequency will lead to low reaction speed and oscillations
High frequency increases computational requirements
The system has a specific time constant (Tau) and having an MPPT faster than Tau is a waste of resources which can lead to instabilities as the variables are read during transients.
=
Oscillations of the system start-up (when the perturbation step is higher) working at 100 Hz. Working at a higher frequency would lead to too early measurements.
10 Hz MPPT
oscillations
Duty cycle is updated
Every 3 MPPT periods, which is 30 ms at 100 Hz

## Slide 12: Hardware current sensor filtering
Different frequencies for different goals:
50 Hz  Low frequency allows reliable MPPT information.
80 kHz  In case a current controller is desired to be implemented, full sensor’s bandwidth is also available.
Further filtering can be achieved
through software
Hysteresis current control,
example of current control
that requires full bandwidth.
Predictive Control of Power Converters and Electrical Drives. P. Cortes. 2012

## Slide 13: Switching frequency
Switching frequency increase:
Switching losses increase.
Higher losses.
Supported by RT-box
Switching frequency decrease:
Component size increase.
Higher cost.

## Slide 14: Bypass diodes vs MICs
Single bypass diode protects one sub-string (20 cells)
If high current flows through shaded cell  Power is consumed instead of produced!
Avoid hot-spots because the power consumed by the cell heats it up.
20% irradiance difference  bypass diode ON
Higher power losses than with MICs
Sub-string

## Slide 15: Bypass diodes vs MICs
Why using MICs improves power extraction?
Demonstration example: shaded cell at 80% irradiance
1st option: Bypass diode ON  9*10% + 1*6.6% = 96.6%
2nd option: Reduce current to 80% 80% of full power
3rd option: MPPT tracker  9*10% + 1*8% = 98%
Using MICs in each PV module  Increases power by 1.4%

## Slide 16: Bypass diodes vs MICs
Why using MICs improves power extraction?
Demonstration example: 30% shaded region
1st option: Bypass diodes ON  9*10% + 1*0% = 90%
2nd option: Reduce current to 70% 70% of full power
3rd option: MPPT tracker  9*10% + 1*7% = 97%
Using MICs in each PV module  Increases power by 7%

## Slide 17: MIC advantage over bypass diode
Power generated in a 3 panel array with ideal bypass diodes.
2 panels 1000 W/m2.
1 panel 400 W/m2 (shaded).
25ºC.
Maximum theoretical power:
Power generated with bypass diodes:
Power generated with a 95% efficient MIC:

## Slide 18: Limitations of single diode PV model
ideal
practical
Not enough with the ideal cell model to define the I-V characteristics of a solar panel because it is an array of series connected cells so it’s necessary to include Rs and Rp!

## Slide 19: Limitations of single diode PV model
Rs  sum of several structural resistances of the PV panel.
Rp  due to the leakage current of the p-n junction and depends on the fabrication method of the cell.
Rp has very high value and Rs very low value (in some cases can be neglected)

## Slide 20: Limitations of single diode PV model
Double diode model:
Extra diode in parallel included to provide an EVEN more accurate I-V characteristic curve
“This model considers the difference in flow of current at low current values due to charge recombination in the semicondictor’s depletion región” (DON’T GET THIS :/)
Higher accuracy with this model BUT increase difficulty to solve the equation  Single diode model is preferred!

## Slide 21: Another MPPT algorithm: Constant voltage
Pro:
Using only a voltage sensor
A simple loop for control
Contra:
The method can’t handle mismatches
Notes: with strong temperature fluctuation the assumption of linear dependence is no longer valid
For a partial shaded PV panel the P-V curve has got multiple local maxima and the method can‘t handle this

## Slide 22: Why bidirectional ?
Extracting and injecting current from the PV panel
Injection current:
1. Because of electroluminescence
the PV panel emits light for
detection microcracks
2. less losses in the system
Bidirectional MIC use

## Slide 23: When does the MIC make sense in terms of cost/energy/efficiency?
Based on a 10 kW series-string MC, or MI PV systems.
One MC or MI for one PV panel
Optimal power production efficiency with missmatches
System cost per watt
System cost
Reference: Efficiency and Cost Trade-Offs for Designing Module Integrated Converter Photovoltaic Systems

## Slide 24: Passive components’ calculations

## Slide 25: Errors in the report
Non inverting buck boost converter is wrong as the ground connection is missing, this happens at least three times in different figures (2.3, 2.4 and 3.1). Page 9,10,17
Calculation of maximum mics (equation 2.2) is wrong. Page 10
The output voltage ripple should be calculated in boost mode at 55V (not at 90V) as the worst case occurs at that point (equation 3.11). Page 18
Because of an early calculation error the output capacitor was calculated to be 130uF not 88uF. Page 19
Wrong legend in ‘valg’ mapping diagram (Figure 5.2). Page 37
Boundary between modes of operation Dbuck=0.079 is wrong it should be Dboost. Page 50
Caption Figure 7.1 should be “Input voltage ringing”. Page 61