## Slide 1: What is a MIC?
Module integrated converter.
Is located next to each PV module.
Prevents mismatch losses.

## Slide 2: MIC advantages
Allows individual maximum power point tracking.
Replaces bypass diode.
Higher efficiencies achieved.
Certain topologies allow bidirectionality.

## Slide 3: Converter design, change random picture

## Slide 4: Power circuitry
Discharging resistors.
Protection diodes.
High frequency capacitors.

## Slide 5: Driving circuitry
Optocouplers for isolation.
Decoupling capacitors.
Current limiting resistors.

## Slide 6: PCB layout
Considerations:
Hot and cold spots.
Isolations.
Interferences.
Others.

## Slide 7: Hot and cold spots
Clear separation of hot and cold sides.
High power.
Low power,
Isolated side.
Low power,
Main side.

## Slide 8: Interferences
Minimal current loops.
Hall sensor location.
Ground planes.
Removed ground plane under inductor.

## Slide 9: Isolations
Isolation bridge under high and low voltage..

## Slide 10: Others
Test points.
Other measuring points and user communication.
Heat sink location.
10mm power traces.